T5 LED Tube

User Manual

Technical Data Sheet

|  | T5-3W | T5-4W | T5-7W | T5-10W | T5-12W | T5-14W | T5-18W |
| --- | --- | --- | --- | --- | --- | --- | --- |
| LED Type | 2835 | 2835 | 2835 | 2835 | 2835 | 2835 | 2835 |
| Rated Luminous Flux | 240lm | 320lm | 560lm | 800lm | 960lm | 1120lm | 1440lm |
| Power Factor | ≥0.90 | ≥0.90 | ≥0.90 | ≥0.90 | ≥0.90 | ≥0.90 | ≥0.90 |
| CCT | 3000K/ 4000K | 3000K/ 4000K | 3000K/ 4000K | 3000K/ 4000K | 3000K/ 4000K | 3000K/ 4000K | 3000K/ 4000K |
| CRI | 80/90 | 80/90 | 80/90 | 80/90 | 80/90 | 80/90 | 80/90 |
| Working Temperature | -20℃~+40℃ (10%~80%RH) | -20℃~+40℃ (10%~80%RH) | -20℃~+40℃ (10%~80%RH) | -20℃~+40℃ (10%~80%RH) | -20℃~+40℃ (10%~80%RH) | -20℃~+40℃ (10%~80%RH) | -20℃~+40℃ (10%~80%RH) |
| Beam Angle | 120° | 120° | 120° | 120° | 120° | 120° | 120° |
| Rated Power | 3W | 4W | 7W | 10W | 12W | 14W | 18W |
| Voltage | ~220V | ~220V | ~220V | ~220V | ~220V | ~220V | ~220V |
| Frequency | 50HZ | 50HZ | 50HZ | 50HZ | 50HZ | 50HZ | 50HZ |
| IP Grade | IP20 | IP20 | IP20 | IP20 | IP20 | IP20 | IP20 |
| Protection Class | Class II | Class II | Class II | Class II | Class II | Class II | Class II |
| Lifespan | 30,000 hrs | 30,000 hrs | 30,000 hrs | 30,000 hrs | 30,000 hrs | 30,000 hrs | 30,000 hrs |
| Dimension (L)*(W)*(H) | 190x22.5x 28.5mm | 296x22.5x 28.5mm | 560x22.5x 28.5mm | 896x22.5x 28.5mm | 960x22.5x 28.5mm | 1120x22.5x 28.5mm | 1440x22.5x 28.5mm |
| Unit N.W. | 0.078kg | 0.124kg | 0.19kg | 0.26kg | 0.28kg | 0.34kg | 0.40kg |
| Material | PC+ Aluminum | PC+ Aluminum | PC+ Aluminum | PC+ Aluminum | PC+ Aluminum | PC+ Aluminum | PC+ Aluminum |

* Built-in constant current driver (with low-voltage, over voltage and over current protection)

Installation:

☞ Please read this manual carefully before installing the led tube, make sure that your operation is safe and correct:

- Please turn off the power before installing the led tube, no need any ballast for this tube

- Make sure that the local input voltage will be suitable for this led tube (~220V)

- When installing the led tubes, no matter what power of each tube, the series connection can not exceed 8 PCS.

Note:

- When opening the package, please check carefully and see if there is any missing part or defective part, if there is any problem, please contact us or the authorized distributor for the replacement.

- The input voltage is ~200V, If exceeding this range, the led tube might be damaged or it can not work probably in a normal state

- Please keep clean the led tube, but never spray water for cleaning

- Please do not put anything to cover the led tube so as to avoid any bad effect for heat dissipation.

5)  If the product is not working or if it doesn’t work in a normal state, please return to the factory or the authorized distributor for repairing. Please do not take apart the led tube by any unprofessional person.

6) When the led tube turns on, please do not look at the light source directly for a long time so as to avoid any harm to your eyes.

7) The working temperature is -20℃~+40℃(10%~80%RH), Please keep out of the direct sunlight, or the lifespan of the product might be decreased.